Cross section descriptions for FE programs

Berthold Höllmann

# Beam direction
## POSEIDON
The x axis is directed along the beam, coinciding with the center of gravity (neutral axis) from the first node the second. The direction node defines local y direction. Direction nodes ``-1'', ``-2'', or ``-3'' define the local y direction in global x, y, or z direction respectively, ``-4'', ``-5'', or ``-6'' define the local y direction in negative global x, y, or z direction respectively.
## Sesam
The x axis is directed along the beam, coinciding with the center of gravity (neutral axis) and pointing from node ``1'' to ``2''. The GUNIVEC record defines local z axis.
## NASTRAN
The x axis is directed along the beam, coinciding with the shear center and pointing from node ``A'' to ``B''. G0, or X1, X2, and X3 describe local y axis.
# Describing beam cross sections in POSEIDON, Sesam, and Patran
## Flat bar

Figure 2.1.1: FB: Cross section dimensions in an POSEIDON flat bar.

Figure 2.1.2: GBARM: Cross section dimensions in Sesam massive bar.

Figure 2.1.3: FB: Cross section dimensions in a NASTRAN flat bar.
## L bar

Figure 2.2.1: L: Cross section dimensions in a POSEIDON L profile section.

Figure 2.2.2: GLSEC: Cross section dimensions in a Sesam L profile section.

Figure 2.2.3: L: Cross section dimensions in a Nastran L profile section.
## T beam

Figure 2.3.1: T: Cross section dimensions in a Poseidon T profile section.

Figure 2.3.2: GIORH: Cross section dimensions in a Sesam GIORH profile section (used to model T sections).

Figure 2.3.3: T: Cross section dimensions in a Nastran T profile section.
## HP profile

Figure 2.4.1: HP: Cross section dimensions in a POSEIDON HP profile section.